## Slide 1: Introduction to CUDA. Part 1
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2016

## Slide 2: Acknowledgements
Many slides are from David Kirk and Wen-mei Hwu’s UIUC course:
    http://courses.engr.illinois.edu/ece498/al/

## Slide 3: GPU Computing History: APIs
2001/2002 – researchers see GPU as data-parallel coprocessor
  The GPGPU field is born
2007 – NVIDIA releases CUDA
  CUDA – Compute Uniform Device Architecture
  GPGPU shifts to GPU Computing
2008 – Khronos releases OpenCL specification
2013 – Khronos releases OpenGL compute shaders
2015 - Khronos releases Vulkan and SPIR-V
Notes: Compute shaders have been in Direct3D for a while.
WebCL never caught on.

## Slide 4: CUDA Terminology
Host – typically the CPU
  Code written in ANSI C
Device – typically the GPU (data-parallel)
  Code written in extended ANSI C
Host and device have separate memories
  Except for SoC
CUDA Program
  Contains both host and device code

## Slide 5: CUDA Terminology
Kernel – data-parallel function
  Invoking a kernel creates lightweight threads on the device
  Threads are generated and scheduled with hardware
Similar to a shader in OpenGL/WebGL/Vulkan.

## Slide 6: CUDA Kernels
Executed N times in parallel by N different CUDA threads
Thread Index
Execution
Configuration
Declaration
Specifier
Notes: threadIdx is a 3-component vector

## Slide 7: CUDA Program Execution
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 8: Thread Hierarchies
Grid – one or more thread blocks
  1D or 2D
Block – array of threads
  1D, 2D, or 3D
  Each block in a grid has the same number of threads
  Each thread in a block can
    Synchronize
    Access shared memory

## Slide 9: Thread Hierarchies
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 10: Thread Hierarchies
Block – 1D, 2D, or 3D
  Example: Index into vector, matrix, volume

## Slide 11: Thread Hierarchies
Thread ID: Scalar thread identifier
Thread Index: threadIdx
1D: Thread ID == Thread Index
2D with size (Dx, Dy)
  Thread ID of index (x, y) == x + y Dx
3D with size (Dx, Dy, Dz)
  Thread ID of index (x, y, z) == x + y Dx + z Dx Dy

## Slide 12: Thread Hierarchies
1 Thread Block
2D Block
2D Index
Notes: Using 2D so does not need to explicitly compute 1D thread ID from x and y

## Slide 13: Thread Hierarchies
Thread Block
  Group of threads
    G80 and GT200: Up to 512 threads
    Fermi, Kepler, Maxwell, Pascal: Up to 1024 threads
  Reside on same processor core
  Share memory of that core

## Slide 14: Thread Hierarchies
Thread Block
  Group of threads
    G80 and GT200: Up to 512 threads
    Fermi, Kepler, Maxwell, Pascal: Up to 1024 threads
  Reside on same processor core
  Share memory of that core
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 15: Thread Hierarchies
Block Index: blockIdx
Dimension: blockDim
  1D or 2D

## Slide 16: Thread Hierarchies
2D Grid
16x16
Threads per block
2D Thread Block

## Slide 17: Thread Hierarchies
Example: N = 32
  16x16 threads per block (independent of N)
    threadIdx ([0, 15], [0, 15])
  2x2 thread blocks in grid
    blockIdx ([0, 1], [0, 1])
    blockDim = 16
i = [0, 1] * 16 + [0, 15]

## Slide 18: Thread Hierarchies
Blocks execute independently
  In any order: parallel or series
  Scheduled in any order by any number of cores
    Allows code to scale with core count

## Slide 19: Thread Hierarchies
Image from: http://developer.download.nvidia.com/compute/cuda/3_2_prod/toolkit/docs/CUDA_C_Programming_Guide.pdf
Notes: Scheduled by the CUDA runtime

## Slide 20: CUDA Memory Transfers
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 21: CUDA Memory Transfers
Host can transfer to/from device
  Global memory
  Constant memory
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 22: CUDA Memory Transfers
cudaMalloc()
  Allocate global memory on device
cudaFree()
  Frees memory
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 23: CUDA Memory Transfers
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 24: CUDA Memory Transfers
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Pointer to device memory
Size in bytes

## Slide 25: CUDA Memory Transfers
cudaMemcpy()
  Memory transfer
    Host to host
    Host to device
    Device to host
    Device to device
Host
Device
Global Memory

## Slide 26: CUDA Memory Transfers
cudaMemcpy()
  Memory transfer
    Host to host
    Host to device
    Device to host
    Device to device
Host
Device
Global Memory

## Slide 27: CUDA Memory Transfers
cudaMemcpy()
  Memory transfer
    Host to host
    Host to device
    Device to host
    Device to device
Host
Device
Global Memory

## Slide 28: CUDA Memory Transfers
cudaMemcpy()
  Memory transfer
    Host to host
    Host to device
    Device to host
    Device to device
Host
Device
Global Memory

## Slide 29: CUDA Memory Transfers
cudaMemcpy()
  Memory transfer
    Host to host
    Host to device
    Device to host
    Device to device
Host
Device
Global Memory

## Slide 30: CUDA Memory Transfers
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Host
Device
Global Memory
Source (host)
Destination (device)
Host to device

## Slide 31: CUDA Memory Transfers
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Host
Device
Global Memory

## Slide 32: Matrix Multiply Reminder
Vectors
Dot products
Row major or column major?
Dot product per output element

## Slide 33: Matrix Multiply
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
P = M * N
Assume M and N are square for simplicity

## Slide 34: Matrix Multiply
1,000 x 1,000 matrix
  1,000,000 dot products
    Each 1,000 multiples and 1,000 adds
Notes: Or 999 adds depending on the code.

## Slide 35: Matrix Multiply: CPU Implementation
Code from: http://courses.engr.illinois.edu/ece498/al/lectures/lecture3%20cuda%20threads%20spring%202010.ppt
void MatrixMulOnHost(float* M, float* N, float* P, int width)‏
{
for (int i = 0; i < width; ++i)‏
for (int j = 0; j < width; ++j)
{
float sum = 0;
for (int k = 0; k < width; ++k)
{
float a = M[i * width + k];
float b = N[k * width + j];
sum += a * b;
}
P[i * width + j] = sum;
}
}
Notes: Row major. The inner most loop goes across a row of M, and down a column of N.

## Slide 36: Matrix Multiply: CUDA Skeleton
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 37: Matrix Multiply
Step 1
  Add CUDA memory transfers to the skeleton

## Slide 38: Matrix Multiply: Data Transfer
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Allocate input
Notes: Error in cudaMalloc calls: should pass address of point, e.g., “(void *)&Md”

## Slide 39: Matrix Multiply: Data Transfer
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Allocate output

## Slide 40: Matrix Multiply: Data Transfer
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 41: Matrix Multiply: Data Transfer
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Read back from device

## Slide 42: Matrix Multiply
Step 2
  Implement the kernel in CUDA C

## Slide 43: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Accessing a matrix, so using a 2D block

## Slide 44: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Each kernel computes one output

## Slide 45: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Where did the two outer for loops in the CPU implementation go?

## Slide 46: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
No locks or synchronization, why?

## Slide 47: Matrix Multiply
Step 3
  Invoke the kernel in CUDA C

## Slide 48: Matrix Multiply: Invoke Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
One block with width by width threads

## Slide 49: Matrix Multiply
What is the major performance problem with our implementation?
What is the major limitation?
Notes: Global memory access
Matrix size is limited by block size

## Slide 50: Matrix Multiply
One Block of threads compute matrix Pd
  Each thread computes one element of Pd
Each thread
  Loads a row of matrix Md
  Loads a column of matrix Nd
  Perform one multiply and addition for each pair of Md and Nd elements
  Compute to off-chip memory access ratio close to 1:1 (not very high)‏
Size of matrix limited by the number of threads allowed in a thread block
Grid 1
Block 1
48
Thread
(2, 2)‏
WIDTH
Md
Pd
Nd
Slide from: http://courses.engr.illinois.edu/ece498/al/lectures/lecture2%20cuda%20spring%2009.ppt