## Slide 1: GPU Architecture Overview
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2016

## Slide 2: Acknowledgements
CPU slides
  Varun Sampath, NVIDIA. Penn alumnus
GPU slides
  Kayvon Fatahalian, CMU
  Mike Houston, NVIDIA

## Slide 3: CPU and GPU Trends
FLOPS – FLoating-point OPerations per Second
GFLOPS - One billion (109) FLOPS
TFLOPS – 1,000 GFLOPS
Notes: FLOPS are not a perfect measurement because of memory access, instruction mix, branches, etc. Peak FLOPS are idealistic, but not often reached in practice. FMA is one instruction.
TFLOPS – 1,000 GFLOPS / 1 trillion FLOPS

## Slide 4
Slide from: http://graphics.cs.cmu.edu/courses/15769/fall2016/lecture/introhwreview/slide_014

## Slide 5: 7.5 TFLOPS in your car!
Image from: http://www.nvidia.com/object/drive-px.html
NVIDIA DRIVE PX 2
  Up to
    2 Tegra SoCs (2.5 TFLOPS)
    2 Pascal GPUs (5 TFLOPS)
Notes: Note that this is multiple GPUs, not one like the Titan on the previous slide.
Fuse data from 12 cameras, lidar, radar, and ultrasonic sensors.
Deep Neural Networks (DNN) for detection and classification.

## Slide 6: CPU and GPU Compute Trends
Chart from: http://docs.nvidia.com/cuda/cuda-c-programming-guide/
Notes: Moore’s Law – the number of transistors on a chip will double about every two year (not 18 months, that was reference to performance)

## Slide 7: FLOP per…
Single-core performance slowing since 2003
  Power and heat limits
GPUs delivery higher FLOP per
  watt
  mm
  dollar
Notes: See http://www.gotw.ca/publications/concurrency-ddj.htm

## Slide 8: CPU and GPU Compute Trends
Chart from: http://docs.nvidia.com/cuda/cuda-c-programming-guide/
Notes: PCI-E Gen3 is 8 GB/s in each direction
2012 CPU: 6-8 core CPU with several MB on-chip cache
Over 400 million CUDA-capable GPUs

## Slide 9: CPU Review
What are the major components in a CPU die?
Notes: Cache, branch predicator, out-of-order logic, ALUs, …

## Slide 10: CPU Review
Desktop Applications
  Lightly threaded
  Lots of branches
  Lots of memory accesses
Profiled with psrun on ENIAC
Slide from Varun Sampath
Notes: Software likes “serial,” hardware likes “parallel.”
Branch prediction accuracy
96.7% - vim
98.9% - ls

## Slide 11: A Simple CPU Core
Image: Penn CIS501
Fetch  Decode  Execute  Memory  Writeback
PC
I$
Register
File
s1
s2
d
D$
+
4
control
Notes: Clocked. All of these steps occur in one clock period.
Clock period bound by datapath delay.
Bad utilization.

## Slide 12: Pipelining
Image: Penn CIS501
PC
Insn
Mem
Register
File
s1
s2
d
Data
Mem
+
4
Tinsn-mem
Tregfile
TALU
Tdata-mem
Tregfile
Tsinglecycle
Notes: About 12-25 gates per-stage, plus 3-5 gates for the latch.
Capitalize on instruction-level parallelism (ILP)
+ Significantly reduced clock period
– Slight latency & area increase (pipeline latches)
? Dependent instructions
? Branches
Alleged Pipeline Lengths:
  Core 2: 14 stages
  Pentium 4 (Prescott): > 20 stages
  Sandy Bridge: in between
Pipelining allows much higher clock speeds.
Pipeline length source: Agner Fog’s Microarchitecture Guide

## Slide 13: Branches
Image: Penn CIS501
jeq loop
???
???
Register
File
S
X
s1
s2
d
Data
Mem
a
d
IR
A
B
IR
O
B
IR
O
D
IR
F/D
D/X
X/M
M/W
nop
Notes: We don’t know what instructions will execute after the branch until the branch is executed. We could either stall until it is, or “speculate” and flush on a misprediction.

## Slide 14: Branch Prediction
+ Modern predictors > 90% accuracy
  Raise performance and energy efficiency
– Area increase
– Potential fetch stage latency increase
Notes:   96.7% accurate on vim example
Flushing a pipeline means a waste of all executed instructions. Area increase potentially even greater for tournament predictors.
Predication avoids explicitly branches completely since the instruction is always fetched and conditionally executed.

## Slide 15: Memory Hierarchy
Memory: the larger it gets, the slower it gets
Rough numbers:
 | Latency | Bandwidth | Size
SRAM (L1, L2, L3) | 1-2ns | 200GBps | 1-20MB
DRAM (memory) | 70ns | 20GBps | 1-20GB
Flash (disk) | 70-90µs | 200MBps | 100-1000GB
HDD (disk) | 10ms | 1-150MBps | 500-3000GB
Notes: SRAM & DRAM latency, and DRAM bandwidth for Sandy Bridge from Lostcircuits
Flash and HDD latencies from AnandTech
Flash and HDD bandwidth from AnandTech Bench
SRAM bandwidth guesstimated.

## Slide 16: Caching
Keep data we need close
Exploit:
  Temporal locality
    Chunk just used likely to be used again soon
  Spatial locality
    Next chunk to use is likely close to previous

## Slide 17: Cache Hierarchy
Hardware-managed
  L1 Instruction/Data caches
  L2 unified cache
  L3 unified cache
Software-managed
  Main memory
  Disk
I$
D$
L2
L3
Main Memory
Disk
(not to scale)
Larger
Faster
Notes: LRU-esque eviction algorithms used for caches. Could be inclusive, exclusive, or neither. OS manages virtual memory.
L1 and L2 generally on-chip. L3 off-chip.

## Slide 18
Intel Core i7 3960X – 15MB L3 (25% of die). 4-channel Memory Controller, 51.2GB/s total
Source: www.lostcircuits.com
Notes: Look at caches – 24.7% of die is L3 cache – 15MB
32KB I$ and 32KB D$
256KB L2 per core
Memory controller – 15% of die; 4 channels, each supporting DDR3-1600  12.8GB/s

## Slide 19: Improving IPC
IPC (instructions/cycle) bottlenecked at 1 instruction / clock
Superscalar – increase pipeline width
Image: Penn CIS371
Notes: Duplicate pipeline registers, execution resources, ports

## Slide 20: Scheduling
Consider instructions:
xor r1,r2 -> r3
add r3,r4 -> r4
sub r5,r2 -> r3
addi r3,1 -> r1
add is dependent on xor (Read-After-Write, RAW)
sub and addi are dependent (RAW)
xor and sub are not (Write-After-Write, WAW)

## Slide 21: Register Renaming
How about this instead:
xor p1,p2 -> p6
add p6,p4 -> p7
sub p5,p2 -> p8
addi p8,1 -> p9
xor and sub can now execute in parallel

## Slide 22: Out-of-Order Execution
Reordering instructions to maximize throughput
Fetch  Decode  Rename  Dispatch  Issue  Register-Read  Execute  Memory  Writeback  Commit
Reorder Buffer (ROB)
  Keeps track of status for in-flight instructions
Physical Register File (PRF)
Issue Queue/Scheduler
  Chooses next instruction(s) to execute
Notes: New pipeline. 3 Principal data structures.
High power-usage since the fetch/decode logic is always executing – and is not powered down like other FUs.
“dispatch logic scales somewhere between quadratically and exponentially with the issue-width” - http://www.lighterra.com/papers/modernmicroprocessors/

## Slide 23: Parallelism in the CPU
Covered Instruction-Level (ILP) extraction
  Superscalar
  Out-of-order
Data-Level Parallelism (DLP)
  Vectors
Thread-Level Parallelism (TLP)
  Simultaneous Multithreading (SMT)
  Multicore

## Slide 24: Vectors Motivation
for (int i = 0; i < N; i++)
A[i] = B[i] + C[i];
Notes: How do we make this go fast?

## Slide 25: CPU Data-Level Parallelism
Single Instruction Multiple Data (SIMD)
  Let’s make the execution unit (ALU) really wide
  Let’s make the registers really wide too
for (int i = 0; i < N; i+= 4) {
// in parallel
A[i] = B[i] + C[i];
A[i+1] = B[i+1] + C[i+1];
A[i+2] = B[i+2] + C[i+2];
A[i+3] = B[i+3] + C[i+3];
}

## Slide 26: Vector Operations in x86
SSE2
  4-wide packed float and packed integer instructions
  Intel Pentium 4 onwards
  AMD Athlon 64 onwards
AVX
  8-wide packed float and packed integer instructions
  Intel Sandy Bridge
  AMD Bulldozer
Notes: Sandy Bridge can issue 2 AVX ops per cycle

## Slide 27: Thread-Level Parallelism
Thread Composition
  Instruction streams
  Private PC, registers, stack
  Shared globals, heap
Created and destroyed by programmer
Scheduled by programmer or by OS

## Slide 28: Simultaneous Multithreading
Instructions can be issued from multiple threads
Requires partitioning of ROB, other buffers
+ Minimal hardware duplication
+ More scheduling freedom for OoO
– Cache and execution resource contention can reduce single-threaded performance
Notes: Register state, return stack buffer, and large page ITLB only replicated stuff: http://www.anandtech.com/show/2594/8

## Slide 29: Multicore
Replicate full pipeline
Sandy Bridge-E: 6 cores
+ Full cores, no resource sharing other than last-level cache
+ Easier way to take advantage of Moore’s Law
– Utilization

## Slide 30: CPU Conclusions
CPU optimized for sequential programming
  Pipelines, branch prediction, superscalar, OoO
  Reduce execution time with high clock speeds and high utilization
Slow memory is a constant problem
Parallelism
  Sandy Bridge-E great for 6-12 active threads
  How about 32K threads?
Notes: A lot of effort put into improving IPC, and avoiding memory latencies. Attacking throughput is an entirely different game.
GeForce GTX 980 – 32K threads

## Slide 31: How did this happen?

## Slide 32: Graphics Workloads
Triangles/vertices and pixels/fragments
Right image from http://http.developer.nvidia.com/GPUGems3/gpugems3_ch14.html

## Slide 33: Early 90s – Pre GPU
Slide from http://s09.idav.ucdavis.edu/talks/01-BPS-SIGGRAPH09-mhouston.pdf
Notes: Wolf 3D – 2.5D. No ceiling and floor height changes (or textures). No rolling walls. No lighting. Enemies always face viewer. Ray casting. Pre-computed texture coordinates.
Doom – Based on BSP tree (Bruce Naylor). Texture mapped all surfaces. Lighting. Varying floor altitudes. Rolling walls.

## Slide 34: Why GPUs?
Graphics workloads are embarrassingly parallel
  Data-parallel
  Pipeline-parallel
CPU and GPU execute in parallel
Hardware: texture filtering, rasterization, etc.

## Slide 35: Data Parallel
Beyond Graphics
  Cloth simulation
  Particle system
  Matrix multiply
Image from: https://plus.google.com/u/0/photos/100838748547881402137/albums/5407605084626995217/5581900335460078306
Notes: Data Parallel – The same program running on multiple data (SPMD).
Cloth is modeled with a mass-spring-damper system obeying Hook’s Law. The force on each mass is computed independently at each time step.
Each particle in a particle system has forces like gravity and wind. Integrating from f = ma to position can be done independently at each time step.
Can an application have more than one type of parallelism?

## Slide 50
Notes: 128 CUDA kernels in parallel

## Slide 71
Notes: Highlight fixed and programmable components