## Slide 1: The Graphics Pipeline
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2016

## Slide 2: Agenda
Graphics Pipeline
Mapping the Graphics Pipeline to Hardware

## Slide 3: Graphics Taxonomy
Graphics
Rendering
Modeling
Animation
Real-Time Rendering
…
…
…

## Slide 4: Graphics Review: Rendering
Rendering
  Goal: Assign color to pixels
Two Parts
  Visible surfaces
    What is in front of what for a given view
  Shading
    Simulate the interaction of material and light to produce a pixel color

## Slide 5: Graphics Pipeline Walkthrough
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Images from http://www.cs.cmu.edu/afs/cs.cmu.edu/academic/class/15869-f11/www/lectures/01_intro.pdf

## Slide 6: Vertex Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Pull together a vertex from one or more buffers
Also called primitive processing (GL ES) or input assembler (D3D)
Image from http://www.virtualglobebook.com/
Framebuffer

## Slide 7: Vertex Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
positions
texture coordinates
OpenGL provides lots of flexibility for pulling vertex attributes from different buffers
For example (no indices):
normal, binormal, bitagent
...
Vertex 0
Framebuffer
Notes: Each attribute can come from a different buffer. Multiple attributes can be interleaved in the same buffer.
What are binormals and bitagents?
What are they used for? Bump mapping, normal mapping. Anything that needs to work in tangent space.
Why do we not need to store all three normal, binormal, and bitagent in the buffer? Because we can compute one from the other two with a cross product.

## Slide 8: Vertex Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
positions
texture coordinates
OpenGL provides lots of flexibility for pulling vertex attributes from different buffers
For example (no indices):
normal, binormal, bitagent
...
Vertex 0
Framebuffer

## Slide 9: Vertex Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
positions
texture coordinates
OpenGL provides lots of flexibility for pulling vertex attributes from different buffers
For example (no indices):
normal, binormal, bitagent
...
Vertex 1
Framebuffer
Notes: Lots more on buffer organization after spring break

## Slide 10: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Pclip = (Mmodel-view-projection)(Pmodel)
Transform incoming vertex position from model to clip coordinates
Perform additional per-vertex computations; modify, add, or remove attributes passed down the pipeline
Formerly called the Transform and Lighting (T&L) stage. Why?
Vertex Shader
Pmodel
Pclip
Vertex Shader
vertex
modified vertex

## Slide 11: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Vertex Shader
vertex
modified vertex
uniforms, e.g.,
matrices, etc.
Pworld = (Mmodel)(Pmodel)
Peye = (Mview) (Pworld)
Pclip = (Mprojection) (Peye)
Model to clip coordinates requires three transforms:
  model to world
  world to eye
  eye to clip
Use 4x4 matrices passed to the vertex shader as uniforms

## Slide 12: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Pworld = (Mmodel)(Pmodel)
Model to world:
Image from http://msdn.microsoft.com/en-us/library/windows/desktop/bb206365(v=vs.85).aspx

## Slide 13: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Peye = (Mview) (Pworld)
  World to eye:
Image from http://www.realtimerendering.com/

## Slide 14: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Pclip = (Mprojection) (Peye)
  Eye to clip coordinates:
Image from http://www.realtimerendering.com/

## Slide 15: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Pclip = (Mmodel-view-projection)(Pmodel)
Pclip = (Mprojection)(Mview)(Mmodel)(Pmodel)
In practice, the model, view, and projection matrices are commonly burnt into one matrix? Why?

## Slide 16: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Transforms demo
Screenshot and demo by Eric Haines.
Notes: Demo and details: http://www.realtimerendering.com/blog/improved-graphics-transforms-demo/

## Slide 17: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Model to clip coordinate transformation is just one use for the vertex shader.
Another use: animation.
How would you implement pulsing?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html

## Slide 18: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
How would you implement pulsing?
Displace position along surface normal over time
How do we compute the displacement?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html
Notes: In what coordinate system do you move the vertex? Model coordinates

## Slide 19: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
How do we compute the displacement?
Consider:
What are the shortcomings?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html
float displacement =
0.5 * (sin(u_time) + 1.0);
Notes: Is [0.0, 1.0] the right displacement range?

## Slide 20: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
How do we compute the displacement?
Consider:
What are the other shortcomings?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html
float displacement =
u_scaleFactor * 0.5 * (sin(u_frequency * u_time) + 1.0);
Notes: Scale and bias sin() from -1.0 to 1.0.
Amplitude may not be enough or too much. Same for frequency.

## Slide 21: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
How do we get the varying bulge?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html

## Slide 22: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
How do we get the varying bulge?
Consider
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter06.html
float displacement =
u_scaleFactor * 0.5 * (sin(position.y * u_frequency * u_time) + 1.0);

## Slide 23: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
What varies per-vertex and what does not?
float displacement =
u_scaleFactor * 0.5 * (sin(position.y * u_frequency * u_time) + 1.0);
Notes: Only position.y varies per-vertex. u_scaleFactor * 0.5 can be pre-computed. u_frequency * u_time can be pre-computed.

## Slide 24: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Vertex Shader
vertex
modified vertex
uniforms
On all modern GPUs, vertex shaders can read from textures as well as uniform variables.
What is this useful for?
textures

## Slide 25: Vertex Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Textures can provide height maps for displacement mapping
Images from http://developer.nvidia.com/content/vertex-texture-fetch

## Slide 26: Vertex Shader
Particle System
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
RenderMonkey Demos
RenderMonkey: http://developer.amd.com/archive/gpu/rendermonkey/pages/default.aspx
Morph
Bounce

## Slide 27: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS
Notes: Perhaps vertices are processed one at a time. Primitive assembly needs to buffer them to form primitives after all vertices for a primitive have been processed
Also called triangle setup

## Slide 28: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS

## Slide 29: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS

## Slide 30: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS

## Slide 31: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS
Primitive Assembly

## Slide 32: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS
Notes: Perhaps vertices are processed in parallel

## Slide 33: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS

## Slide 34: Primitive Assembly
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A vertex shader processes one vertex. Primitive assembly groups vertices forming one primitive, e.g., a triangle, line, etc.
VS
Primitive Assembly

## Slide 35: Perspective Division and Viewport Transform
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
There are a series of stages between primitive assembly and rasterization.
  Perspective division
  Viewport transform
Pndc = (Pclip).xyz / (Pclip).w
Image from http://www.realtimerendering.com/
Pwindow = (Mviewport-transform)(Pndc)
Notes: What is the z component of window coordinates used for?

## Slide 36: Clipping
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
There are a series of stages between primitive assembly and rasterization.
  Clipping
Image from http://www.realtimerendering.com/
Notes: Clipping may happen sooner in the pipeline, but GL 4.2 shows it as happening after the viewport transform

## Slide 37: Rasterization
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Determine what pixels a primitive overlaps
How would you implement this?
What about aliasing?
What happens to non-position vertex attributes during rasterization?
What is the triangle-to-fragment ratio?
Notes: Attributes are interpolated across the primitive (unless explicitly told otherwise).
There are usually many more fragments than triangles creating an irregular workload.
Rasterization can be done with a scanline algorithm or hierarchically (or recursive flood fill, in theory).
Demo with AA and more: http://acko.net/files/fullfrontal/fullfrontal/webglmath/pixels.html
From Larrabee (http://www.student.chemia.uj.edu.pl/~mrozek/USl/wyklad/Nowe_konstrukcje/Siggraph_Larrabee_paper.pdf):
  “Our algorithm is a highly optimized version of the recursive descent algorithm described by Greene [1996]. The basic idea is to convert clipped triangles to screen space, then compute a halfplane equation for each triangle edge [Pineda 1988]. This lets us determine if a rectangular block is entirely inside the triangle, entirely outside the triangle, or partially covered by the triangle. In the latter case, the algorithm subdivides the block recursively until it is reduced to an individual pixel or sample position. “

## Slide 38: Fragment Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Shades the fragment by simulating the interaction of light and material
Loosely, the combination of a fragment shader and its uniform inputs is a material
Also called a Pixel Shader (D3D)
Fragment shaders can be computationally intense
What exactly is the fragment input?
What are examples of useful uniforms? Useful textures?
Fragment Shader
fragment
fragment’s color
uniforms
textures
Notes: Fragment input: (x_window, y_window, z_window a.k.a. depth) and interpolated varyings (attributes) from rasterization
Useful uniforms: lights, time, etc.
Useful textures: diffuse map, bump map, specular, map, etc.

## Slide 39: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Blinn-Phong Lighting
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter05.html
float diffuse =
max(dot(N, L), 0.0);
Fragment Shader
Rasterizer
Notes: Diffuse light scatters in all directions; rough surfaces.

## Slide 40: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Blinn-Phong Lighting
Why not evaluate per-vertex and interpolate during rasterization?
Image from http://http.developer.nvidia.com/CgTutorial/cg_tutorial_chapter05.html
float specular =
max(pow(dot(H, N), u_shininess), 0.0);
Fragment Shader
Rasterizer
Notes: H = (V + L) / 2. Constant for all fragments for a directional light source.
Specular light is for mirror reflection; shiny and smooth surfaces. Shininess controls the tightest of the specular bump.

## Slide 41: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Per-fragment vs. per-vertex lighting
Which is which?
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Fragment Shader
Rasterizer
Notes: Per-fragment on left
Demo: http://www.realtimerendering.com/udacity/?load=demo/unit1-teapot-demo.js

## Slide 42: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Texture Mapping
Image from http://www.realtimerendering.com/
Fragment Shader
Rasterizer

## Slide 43: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Lighting and texture mapping
Fragment Shader
Rasterizer
Image from http://www.virtualglobebook.com/

## Slide 44: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Bump mapping
Fragment Shader
Rasterizer

## Slide 45: Fragment Shader
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Bump mapping
Fragment Shader
Rasterizer

## Slide 46: Fragment Shader
Example: Specular map
Vertex Shader
Primitive Assembly
Rasterizer
Blend
Vertex Assembly
Framebuffer
Fragment Shader
Per-Fragment Tests
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Notes: Demo: http://www.realtimerendering.com/udacity/index_solutions.html?load=unit8/ps-specular-mapping_sol.js

## Slide 47: Fragment Shader
Example: Non-Photorealistic Rendering (NPR)
Vertex Shader
Primitive Assembly
Rasterizer
Blend
Vertex Assembly
Framebuffer
Fragment Shader
Per-Fragment Tests
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Notes: Two-tone shading.
Also common to shade silhouettes.
Demo: http://www.realtimerendering.com/udacity/unit9/two-tone-shading_sol/index.html

## Slide 48: Fragment Shader
Example: Reflection mapping
Vertex Shader
Primitive Assembly
Rasterizer
Blend
Vertex Assembly
Framebuffer
Fragment Shader
Per-Fragment Tests
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Notes: Demo: http://www.realtimerendering.com/udacity/index_solutions.html?load=unit8/ps-reflection-mapping_sol.js

## Slide 49: Fragment Shader
More examples
Vertex Shader
Primitive Assembly
Rasterizer
Blend
Vertex Assembly
Framebuffer
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Fragment Shader
Per-Fragment Tests
Fog
Notes: Fog demo: https://www.udacity.com/course/viewer#!/c-cs291/l-124106593/m-170440734

## Slide 50: Fragment Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A fragment shader can output color, but what else would be useful?

## Slide 51: Fragment Shader
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A fragment shader can output color, but what else would be useful?
  Discard the fragment. Why?
  Depth. Why?
  Multiple colors. Why?

## Slide 52: Vertex and Fragment Shader Examples
By Steven Wittens, @unconed
Notes: Demo: http://acko.net/files/fullfrontal/fullfrontal/webglmath/shaders.html

## Slide 53: Per-Fragment Tests
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
A fragment must go through a series of tests to make to the framebuffer
  What tests are useful?

## Slide 54: Scissor Test
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Scissor Test
Stencil Test
Depth Test
Discard a fragment if it is within a rectangle defined in window coordinates
  Why is this useful?
  Does this need to happen after fragment shading?

## Slide 55: Scissor Test
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Scissor Test
Stencil Test
Depth Test
The scissor test is useful for “scissoring out” parts of the window that do not need to be shaded
  For performance. Why?
  Post-processing effects
  Multipass rendering
Notes: Scissor out area that affects a light or a post-processing effect, e.g., fixing cracks in screen-space. Project bounding volume onto near plane.

## Slide 56: Stencil Test
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Scissor Test
Stencil Test
Depth Test
The stencil test can discard arbitrary areas of the window, and count per-fragment
A stencil is written to the stencil buffer, and later fragments can be tested against this buffer
What is this useful for?
Notes: Multi-pass avoid z-fighting (decaling)
Stencil shadow volumes – inc on entrance, dec on exit.

## Slide 57: Depth Test
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Finds visible surfaces
Once called “ridiculously expensive”
Also called the z-test
  Does it need to be after fragment shading?
Scissor Test
Stencil Test
Depth Test
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
z-fighting
Notes: Memory densities went up. Cost went down. Z-buffer is efficient to implement in hardware. Has lots of optimizations.
z-fighting demo: http://www.realtimerendering.com/udacity/?load=demo/unit2-z-fighting.js

## Slide 58: Depth Test
Image from http://www.virtualglobebook.com/

## Slide 59: Depth Test
Image from http://www.virtualglobebook.com/

## Slide 60: Blending
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Combine fragment color with framebuffer color
  Can weight each color
  Can use different operations: +, -, etc.
Why is this useful?
Fragment Shader
Rasterizer

## Slide 61: Blending
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Example: Translucency
Additive Blending
Alpha Blending
Fragment Shader
Rasterizer
Cdest = (Csource.rgb)(Csource.a) +
(Cdest.rgb) (1 - Csource.a);
Cdest = (Csource.rgb)(Csource.a) + (Cdest.rgb);
Image from http://http.developer.nvidia.com/GPUGems/gpugems_ch06.html
Notes: Also see this demo: http://www.andersriggelsen.dk/glblendfunc.php

## Slide 62: Blending
Vertex Shader
Primitive Assembly
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Alpha Blending sorting
Fragment Shader
Rasterizer
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Notes: Alpha Blending requires sorting back to front
Demo: http://www.realtimerendering.com/udacity/?load=demo/unit3-transparency.js

## Slide 63: Graphics Pipeline Walkthrough
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Images from http://www.cs.cmu.edu/afs/cs.cmu.edu/academic/class/15869-f11/www/lectures/01_intro.pdf
After all that, write to the framebuffer!

## Slide 64: Example Performance Analysis
Images from http://www.student.chemia.uj.edu.pl/~mrozek/USl/wyklad/Nowe_konstrukcje/Siggraph_Larrabee_paper.pdf
Notes: F.E.A.R -> stencil shadows. Less fragment shading load, but more rasterization and depth test. Dynamically allocating compute resources benefits this.
Pixel setup = interpolation.

## Slide 65: Evolution of the Programmable Graphics Pipeline
Pre GPU
Fixed function GPU
Programmable GPU
Unified Shader Processors

## Slide 66: Early 90s – Pre GPU
Slide from http://s09.idav.ucdavis.edu/talks/01-BPS-SIGGRAPH09-mhouston.pdf
Notes: Wolf 3D – 2.5D. No ceiling and floor height changes (or textures). No rolling walls. No lighting. Enemies always face viewer. Ray casting. Pre-computed texture coordinates.
Doom – Based on BSP tree (Bruce Naylor). Texture mapped all surfaces. Lighting. Varying floor altitudes. Rolling walls.

## Slide 67: Why GPUs?
Exploit Parallelism
  Pipeline parallel
  Data-parallel
  CPU and GPU executing in parallel
Hardware:
  Texture filtering, rasterization, alpha blending, …
  MAD, sqrt, ...
Notes: Rasterization and interpolation.

## Slide 68: Texture Hardware
Screenshot and demo by Eric Haines and Gundega Dekena. Udacity Interactive 3D Graphics.
Wrap modes
Texture filtering
Software is 12-40x slower (Larrabee)
Notes: Wrap mode demos: https://www.udacity.com/course/viewer#!/c-cs291/l-124106595/m-176364092
Filtering demo: https://www.udacity.com/course/viewer#!/c-cs291/l-124106595/m-176452098
Bonus – anisotropy: https://www.udacity.com/course/viewer#!/c-cs291/l-124106595/m-176170989
Larrabee paper: http://www.student.chemia.uj.edu.pl/~mrozek/USl/wyklad/Nowe_konstrukcje/Siggraph_Larrabee_paper.pdf
  “Larrabee includes texture filter logic because this operation cannot be efficiently performed in software on the cores. Our analysis shows that software texture filtering on our cores would take 12x to 40x longer than our fixed function logic, depending on whether decompression is required. There are four basic reasons:
  * Texture filtering still most commonly uses 8-bit color components, which can be filtered more efficiently in dedicated logic than in the 32-bit wide VPU lanes.
  * Efficiently selecting unaligned 2x2 quads to filter requires a specialized kind of pipelined gather logic.
  * Loading texture data into the VPU for filtering requires an impractical amount of register file bandwidth.
  * On-the-fly texture decompression is dramatically more efficient in dedicated hardware than in CPU code.
  The Larrabee texture filter logic is internally quite similar to typical GPU texture logic. It provides 32KB of texture cache per core and supports all the usual operations, such as DirectX 10 compressed texture formats, mipmapping, anisotropic filtering, etc. Cores pass commands to the texture units through the L2 cache and receive results the same way. The texture units perform virtual to physical page translation and report any page misses to the core, which retries the texture filter command after the page is in memory. Larrabee can also perform texture operations directly on the cores when the performance is fast enough in software. “

## Slide 69: 3dfx Voodoo (1996)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Still
Software
Hardware
Image from http://www.thedodgegarage.com/3dfx/v1.htm
In hardware:
Fixed-function rasterization, texture mapping, depth testing, etc.
4 - 6 MB memory
PCI bus
$299
Notes: Voodoo was started by SGI alums in 1994. IP acquired by NVIDIA in 2002.
Could only read from one texture
Required separate VGA card for 2D

## Slide 70: Aside: Mario Kart 64
Image from http://www.gamespot.com/users/my_shoe/
High fragment load / low vertex load
Notes: Release Dec, 1996 (Japan). Same era as Voodoo
Used SGI chip. Even though the vertex load is low, it is done in hardware

## Slide 71: Aside: Mario Kart Wii
High fragment load / low vertex load?
Image from http://wii.ign.com/dor/objects/949580/mario-kart-wii/images/

## Slide 72: NVIDIA GeForce 256 (1999)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Hardware
Image from http://en.wikipedia.org/wiki/File:VisionTek_GeForce_256.jpg
In hardware:
Fixed-function vertex shading (T&L)
Multi-texturing: bump maps, light maps, etc.
10 million polygons per second
Direct3D 7
AGP bus
Notes: Not all games use hardware T&L

## Slide 73: NVIDIA GeForce 3 (2001)
Vertex Shader
Primitive Assembly
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Hardware
Optionally bypass fixed-function T&L with a programmable vertex shader
Optionally bypass fixed-function fragment shading with a programmable fragment shader (register combiners)
Many programming limits
Direct3D 8
Pentium IV – 20 stages
GeForce 3 – 600-800 stages
Fixed-function stage
Programmable stage
Fragment Shader

## Slide 74: NVIDIA GeForce 6 (2004)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Hardware
Much better programmable fragment shaders
Vertex shader can read textures
Dynamic branches
Multiple render targets
PCIe bus
OpenGL 2 / Direct3D 9
textures

## Slide 75: NVIDIA GeForce 6 (2004)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Vertex shader can read textures
Dynamic branches
Multiple render targets
PCIe bus
OpenGL 2 / Direct3D 9
Image from ftp://download.nvidia.com/developer/presentations/2004/GPU_Jackpot/Shader_Model_3.pdf

## Slide 76: NVIDIA GeForce 6 (2004)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Vertex shader can read textures
Dynamic branches
Multiple render targets
PCIe bus
OpenGL 2 / Direct3D 9
Image from ftp://download.nvidia.com/developer/presentations/2004/GPU_Jackpot/Shader_Model_3.pdf
Notes: Application only renders a single quad
Pixel shader calculates intersection between view ray
and bounding box, discards pixels outside
Marches along ray between far and near intersection
points, accumulating color and opacity
Looks up in 3D texture, or evaluates procedural function at
each sample
Compiles to REP/ENDREP loop
Allows us to exceed the 512 instruction PS2.0 limit
All blending is done at fp32 precision in the shader
100 steps is interactive on 6800 Ultra

## Slide 77: Dynamic Branches
Image from http://developer.amd.com/media/gpu_assets/03_Clever_Shader_Tricks.pdf

## Slide 78: Dynamic Branches
For best performance, fragment shader dynamic branches should be coherent in screen-space
How does this relate to warp partitioning in CUDA?

## Slide 79: NVIDIA GeForce 6 (2004)
Image from http://http.developer.nvidia.com/GPUGems2/gpugems2_chapter30.html
6 vertex
shader processors
16 fragment
shader processors

## Slide 80: NVIDIA GeForce 8 (2006)
Vertex Shader
Primitive Assembly
Fragment Shader
Rasterizer
Per-Fragment Tests
Blend
Vertex Assembly
Framebuffer
Ground-up GPU redesign
Geometry Shaders
Transform-feedback
OpenGL 3 / Direct3D 10
Unified shader processors
Support for GPU Compute
Geometry Shader

## Slide 81: Geometry Shaders
Image from David Blythe : http://download.microsoft.com/download/f/2/d/f2d5ee2c-b7ba-4cd0-9686-b6508b5479a1/direct3d10_web.pdf

## Slide 82: NVIDIA G80 Architecture
Slide from http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf

## Slide 83: Why Unify Shader Processors?
Slide from http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf

## Slide 84: Why Unify Shader Processors?
Slide from http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf

## Slide 85: Evolution of the Programmable Graphics Pipeline
Slide from Mike Houston: http://s09.idav.ucdavis.edu/talks/01-BPS-SIGGRAPH09-mhouston.pdf

## Slide 86: Evolution of the Programmable Graphics Pipeline
Slide from Mike Houston: http://s09.idav.ucdavis.edu/talks/01-BPS-SIGGRAPH09-mhouston.pdf
Notes: Mobile made fixed function important again: fewer transistors, lower power, better performance.